## Slide 1: Good practice proposal – Building one access point to dispersed data sources
Marcin Grudzień Pushing WMS services to their limits 8th February 2022

## Slide 2: Description of the GP (1)
Datasets maintained at a local level independently by different municipalities often:
Are very similar: have the same content, data model, structure, portrayal etc.
Have different spatial extend limited by boundaries of municipalities
A good example is cadastral data in Poland that is maintained by 380 counties (powiaty)
Counties maintain the cadastral datasets in the same national data model
Each county maintains a cadastral dataset limited spatially to its boundaries
Each county is obliged by law to publish network services providing dataset the county maintains
This results in 380 WMS services published by districts providing cadastral datasets

## Slide 3: Description of the GP (2)
Let’s create a proxy, collective service that integrates local services
Originator and author of collective services is Professor Waldemar Izdebski

## Slide 4: Benefits
One endpoint for a particular dataset (e.g. cadastre) for the entire country
It saves user’s time – the user doesn't have to search for endpoints of view services published by different counties
It hides the complexity of the SDI implementation – from the user perspective, integrated service provides access to one seamless dataset

## Slide 5: Intendent outcome
Users should access dispersed datasets from a single endpoint
This can be, for example, done as:
a single national endpoint per dataset integrating services published by municipalities
a single European access point per INSPIRE theme integrating services provided by the Member States

## Slide 6: How it works? (1)
Request forwarded to many local services
WMS client application
Collective, proxy WMS service
Spatial extends of counties
First local WMS service
Second local WMS service
Third local WMS service
1 – GetMap WMS Request
2 – GetMap WMS
request
3 –GetMap WMS
response
5 – GetMap WMS
response
4 – Merging (flattening) of local services WMS GetMap responses

## Slide 7: How it works? (2)
Request forwarded to one local service
WMS client application
Collective, proxy WMS service
Spatial extends of counties
First local WMS service
Second local WMS service
Third local WMS service
1 – GetMap WMS Request
2 – 302 redirection
GetMap WMS
response containing
request URL
to the local service
3 – GetMap WMS request
4 –GetMap WMS response

## Slide 8: Evidence of implementation (1)
There are the following integrating WMS services available:
KIEG – cadastral data (cadastral parcels and buildings) https://integracja.gugik.gov.pl/cgi-bin/KrajowaIntegracjaEwidencjiGruntow
KIUT – utility infrastructure data (electricity, water, telecommunication, sewers, gas and other networks) https://integracja.gugik.gov.pl/cgi-bin/KrajowaIntegracjaUzbrojeniaTerenu
KIBDOT – large scale topographic data (containing the location of fences, trees, curbs, etc. ) https://integracja.gugik.gov.pl/cgi-bin/KrajowaIntegracjaBazDanychObiektowTopograficznych
KIMP – local development plans https://mapy.geoportal.gov.pl/wss/ext/KrajowaIntegracjaMiejscowychPlanowZagospodarowaniaPrzestrzennego
KISKZP – local land use study https://mapy.geoportal.gov.pl/wss/ext/KrajowaIntegracjaStudiumKierunkowZagospodarowaniaPrzestrzennego

## Slide 9: Evidence of implementation (2)
Number of integrated local services
KIEG – 380 counties
KIUT – 380 counties
KIBDOT – 126 counties
KIMP – 1564 communes
KISKZP – 1052 communes

## Slide 10: Evidence of implementation (3)
INSPIRE themes covered
Administrative units
Cadastral parcels
Hydrography
Transport networks
Elevation
Land cover
Buildings
Land use
Soil
Utility and governmental services

## Slide 11: Evidence of implementation (4)
KIEG
KIUT
KIBDOT
KIMP
KISKZP

## Slide 12: Evidence of implementation (5)
Chart: Number of monthly requests to the KIEG service
| 2017-07 | 2017-08 | 2017-09 | 2017-10 | 2017-11 | 2017-12 | 2018-01 | 2018-02 | 2018-03 | 2018-04 | 2018-05 | 2018-06 | 2018-07 | 2018-08 | 2018-09 | 2018-10 | 2018-11 | 2018-12 | 2019-01 | 2019-02 | 2019-03 | 2019-04 | 2019-05 | 2019-06 | 2019-07 | 2019-08 | 2019-09 | 2019-10 | 2019-11 | 2019-12 | 2020-01 | 2020-02 | 2020-03 | 2020-04 | 2020-05 | 2020-06 | 2020-07 | 2020-08 | 2020-09 | 2020-10 | 2020-11 | 2020-12 | 2021-01 | 2021-02 | 2021-03 | 2021-04 | 2021-05 | 2021-06 | 2021-07 | 2021-08 | 2021-09 | 2021-10 | 2021-11 | 2021-12
 | 312021 | 391790 | 3500414 | 45631671 | 45505116 | 40690961 | 56368593 | 53327146 | 53725199 | 53606817 | 54268821 | 53122887 | 67375698 | 71659708 | 63589486 | 64584925 | 81537010 | 66062174 | 91159102 | 101710022 | 123069412 | 132310323 | 135060504 | 108625792 | 140715690 | 134683079 | 140713122 | 153498386 | 146892553 | 121135083 | 162086181 | 163494710 | 156207662 | 156097550 | 189447919 | 172025911 | 172580587 | 182141082 | 199619863 | 197415297 | 207202667 | 185389163 | 225916555 | 211719743 | 285085480 | 278631617 | 268724895 | 220260418 | 218591281 | 188412291 | 222546278 | 233891770 | 232199326 | 197809898
Till the end of 2021, there were 7.3 billion requests to KIEG service.

## Slide 13: Other relevant information
Standardisation of local network services
The standards are available for
  KIEG
  KIUT
Validator application

## Slide 14: Limitations
Additional resources are required to:
create and maintain a proxy service
develop standardisation documents
standardise local services

## Slide 15: Sample implementation
Our approach
  Sample service implemented integrating local WMSs from three counties
    The sample service is available at http://185.238.72.102/cgi-bin/wmssampleintegration
  As simple as possible
  Everything documented on GitHub
  Config files and documentation contains all information necessary to integrate WMS services of your choice
  Based on modified MapServer

## Slide 16: GitHub documentation
GitHub documentation contains step by step information on
  installing modified MapServer
  setting up collective service
  sample configuration files
  modified MapServer, including source codes
In addition, the documentation explains the “logic” of how a collective service operates

## Slide 17: WMS server
The service is published by modified MapServer v7.0.7.
Tested on Debian 9 and Apache Server
  In the case of other Linux distributions, web servers or Debian versions, some modifications of installation procedure or code may be required

## Slide 18: WMS server - modifications
Following modifications/optimisations have been implemented:
Modified spatial extend of the WMS service. The standard version of MapServer allows defining the spatial extent of WMS service source as a bounding box. Modified version allows setting spatial extent of local WMS service using a dedicated parameter containing polygon geometry. MapServer will request the local WMS service only when the map view overlaps that polygon, thus reducing network traffic.
Redirection mechanism. If a request covers the spatial extend of only one local service, the collective service does not forward the request to the local service. Still, it returns to the client application proper URI pointing directly to a local service.
Cookies support. Some local servers may require sending additional information stored in cookies. Modified MapServer allows adding cookies to requests.
Grouping of layers. Request to different layers of the same WMS local service is aggregated. Instead of many requests, one separately for each layer, one request to a WMS local service is sent.

## Slide 19: WMS server – additional parameters
Two parameters have been added to the standard MapServer distribution
gs_bounds – defines the spatial extent of local service
gs_sendUrl – defines whether the 302 redirections are supported

## Slide 20: WMS server – requests handling
Server
WMS client application
Bash script
A website containing information about the service
(optional)
No parameters
The static file containing modified/simplified GetCapabilities response
GetCapabilities
Custom script integrating GFI responses of local services *
GetFeatureInfo
Handled by modified Map Server
Other including
GetMap
* Support of GFI not implemented in sample service

## Slide 21: Summary
Integration of local services improve their usability
Transparent from a user perspective
Reproducible and customisable
  Can be applied in regional, national and international use cases
More on https://github.com/INSPIRE-MIF/gp-single-access-point

## Slide 22: Live demo

## Slide 23: Acknowledgments
GUGiK Team:
Waldemar Izdebski
Piotr Perz
Ewa Surma
Jarosław Zembrzuski
Aneta Seremet with team
Anna Bober
Ryszard Bojarski
And others
JRC Team:
Jordi Escriu
Alexander Kotsev

## Slide 24
Thank you for your attention
Questions?
marcin.grudzien@gugik.gov.pl